## Slide 1: Computer Networks & Architecture
Unit 1: Fundamentals of Network Communications

## Slide 2: Network Types & Classifications
Networks are categorized based on geographic scale and infrastructure:
Local Area Network (LAN)
  Covers a small area such as a home, office, or university campus
  High data transfer rates (1 Gbps to 10 Gbps) with low latency
Metropolitan Area Network (MAN)
  Spans a city or regional district connecting enterprise branches
Wide Area Network (WAN)
  Spans national or global distances using telco backbones and fiber

## Slide 3: OSI vs TCP/IP Protocol Architecture
Layer Tier | OSI 7-Layer Reference | TCP/IP 4-Layer Suite
Application & UI | Application, Presentation, Session | Application (HTTP, DNS, SSH)
End-to-End Transport | Transport Layer (TCP, UDP flow control) | Transport Layer (TCP, UDP)
Packet Routing | Network Layer (Logical IP addressing) | Internet Layer (IPv4, IPv6, ICMP)
Notes: Instructor Note: Clarify that OSI is a conceptual model, whereas TCP/IP is the practical Internet protocol suite.

## Slide 4: Physical Transmission Media Comparison
Media Category | Typical Bandwidth | Max Distance | Noise Immunity
Cat6a Twisted Pair | 10 Gbps | 100 meters | Moderate (UTP/STP)
Coaxial Cable | 1 Gbps | 500 meters | Good shielding
Single-mode Fiber | 100+ Gbps | 40+ kilometers | Immune (Light pulses)